## Slide 1
FPGA PROFESSIONAL ASSOCIATION · AI-AUGMENTED SYSTEMS ENGINEERING
WEEK 6 OF 15
Design-Space Exploration & Trade Studies
Multi-objective optimization; Pareto analysis; weighted trade studies and AHP; AI as explorer of large design spaces.
FPGA Professional Association · AI-Augmented Systems Engineering · Week 6
1

## Slide 2
WEEK 6 · SESSION PLAN
Today's Agenda & Objectives
Session agenda
1
Multi-Objective Reality
2
Trade-Study Method
3
AI as Design-Space Explorer
4
Choosing the Operating Point
5
Studio activity & discussion
6
Deliverables & next week
By the end of this session, you can
Formulate a multi-objective design problem and characterize its Pareto frontier.
Conduct a weighted trade study and an Analytic Hierarchy Process comparison, with sensitivity analysis.
Use surrogate models, Bayesian optimization, and generative methods as design-space explorers.
Select and justify an operating point on the frontier against stakeholder value.
FPGA Professional Association · AI-Augmented Systems Engineering · Week 6
2

## Slide 3
WEEK 6 · CONCEPT 1 OF 4
Multi-Objective Reality
1.1
Single-objective optimization is a textbook fiction; real systems trade performance, cost, mass, schedule, and risk simultaneously.
1.2
A design is Pareto-optimal when no objective can improve without another worsening — the frontier is the set of defensible answers.
1.3
Everything off the frontier is dominated; everything on it is a values question, not a math question.
FPGA Professional Association · AI-Augmented Systems Engineering · Week 6
3

## Slide 4
WEEK 6 · CONCEPT 2 OF 4
Trade-Study Method
Define criteria and measures first, alternatives second — reversing the order launders a pre-made decision.
2.2
Weighted-sum scoring is transparent and fragile; AHP structures pairwise judgments and exposes inconsistency.
2.3
Sensitivity analysis is the integrity check: if the winner flips under small weight changes, report the flip, not just the winner.
FPGA Professional Association · AI-Augmented Systems Engineering · Week 6
4

## Slide 5
WEEK 6 · CONCEPT 3 OF 4
AI as Design-Space Explorer
3.1
Surrogate models learn cheap approximations of expensive analyses, letting search visit thousands of candidates per hour.
3.2
Bayesian optimization spends its expensive evaluations where uncertainty and promise are highest.
3.3
Generative methods propose configurations humans wouldn't sketch — widening the frontier, and the review burden with it.
FPGA Professional Association · AI-Augmented Systems Engineering · Week 6
5

## Slide 6
WEEK 6 · CONCEPT 4 OF 4
Choosing the Operating Point
The frontier answers what is possible; stakeholder value answers what is preferred — no algorithm supplies the preference.
4.2
Document the choice as a decision record: alternatives, criteria, weights, sensitivity, and the rationale in plain language.
4.3
Revisit points when assumptions move: a frontier computed on last year's costs is last year's frontier.
FPGA Professional Association · AI-Augmented Systems Engineering · Week 6
6

## Slide 7
WEEK 6 · THE AI LENS
Where AI Enters This Week
As a Tool
Surrogates, Bayesian search, and generative design multiply how much of the space you can afford to see.
As a Component
If the shipped product optimizes online (adaptive control, dynamic pricing of resources), its objective function is a requirement.
The Human Residual
Framing objectives and constraints, auditing surrogate validity, and making the value call the frontier cannot make.
One question, every week: which mode is this — and what human role does it leave behind?
FPGA Professional Association · AI-Augmented Systems Engineering · Week 6
7

## Slide 8
WEEK 6 · APPLICATIONS
Across the Disciplines
Mechanical
Heat exchanger: effectiveness vs. mass vs. cost — a three-way frontier every student can compute.
Aerospace
Generative wing structures: the optimizer's organic shapes still face the certification question.
Energy
Microgrid sizing: storage vs. generation vs. resilience under uncertain demand.
Biomedical
Prosthetic design: weight, strength, and cost trade directly against patient outcomes.
FPGA Professional Association · AI-Augmented Systems Engineering · Week 6
8

## Slide 9
WEEK 6 · STUDIO
In-Class Activity & Discussion
Studio activity
Pareto lab: from a provided 40-alternative dataset (three objectives), identify the frontier, run a weighted study with sensitivity, and defend your operating point in one slide.
Seminar discussion
Q1
When has a “best design” in your field turned out to be someone's unexamined weighting?
Q2
Should a generative design no engineer can fully explain be allowed on the frontier at all?
FPGA Professional Association · AI-Augmented Systems Engineering · Week 6
9

## Slide 10
WEEK 6 · WRAP
Before Next Week
Read
Kossiakoff ch.9 (trade studies); INCOSE Hdbk (decision management); SEBoK decision-analysis articles.
Due
PS-2 due. Project D2 due: architecture + function-allocation matrix.
Next week
Week 7 — Graph-Theoretic Foundations for Systems Analysis. Systems as graphs; DSM and N-squared analysis; partitioning and clustering; critical-path and network methods; graph neural networks.
FPGA Professional Association · AI-Augmented Systems Engineering · Week 6
10